## Slide 1: Global vs. Local pMOR
Hritik Singh, Raúl San Miguel Peñas
Supervisor: Sebastian Schopper
TUM School of Engineering and Design
Chair of Structural Mechanics
Munich, 13 February 2023

## Slide 2: Motivation
Complex and large numerical models require substantial computational power and large amount of memory
Model Order Reduction techniques allow to reduce these requirements at the cost of an approximation of full system
However, the reduced model becomes invalid when parameters of the original model such as material properties, the geometry or boundary conditions are changed
Some applications like optimization, navigation, etc. require repeated model evaluations over a large range of such parameter values

## Slide 3: Motivation
A naïve approach would be to generate a reduced order model (ROM) at each queried point in the parameter space
However, this is a costly task requiring large computations with full order system, thus generally unfeasible
Parametric Model Order Reduction (pMOR) helps in overcoming these problems
In pMOR, instead of generating ROMs at each point, a sampling at different parameter combinations is done to generate a database of reduced quantities
Two main techniques – Global pMOR and Local pMOR

## Slide 4: Global pMOR
In global pMOR, the reduced bases obtained at sampling points are combined into one global basis matrix
The global basis matrix can then be reduced further using SVD to with r most important bases
Final reduced system: , , ,
This is easy to implement but the parametric reduced model grows with the number of samples
Also, it requires reduced bases to be on the same mesh as sample points

## Slide 5: Local pMOR
In local pMOR, interpolation of the reduced matrices is done to avoid full order systems
However, a straightforward interpolation of the reduced matrices is not meaningful because the reduced matrices relate to different reduced bases
Therefore, a generalized coordinate system is computed first, followed by the transformation of reduced matrices to this system
where is obtained by SVD,
Transformation matrix:
, , ,
The evaluation efficiency is higher than global pMOR since the parametric reduced model doesn’t grow with the number of samples
But the reduced bases still need to be generated on the same mesh as sample points

## Slide 6: Local pMOR Interpolation

## Slide 7: Methodology
Generate a FEM model of the Timoshenko cantilever beam at different parameter samples (e.g. different beam lengths and thicknesses)
Perform MOR at each parameter sample using SO-IRKA
Collect reduced model bases together to obtain a parametric model
Reduce the parametric model using either global or local pMOR technique
Interpolation in the case of local pMOR has been done using cubic splines
Solve the reduced system model at required parameter value
Obtain the frequency response for a sweep of frequencies

## Slide 8: Second Order Iterative Rational Krylov Alogrithm (SO-IRKA)
Useful for MOR of single-input single-output (SISO) second order systems
Starts with an initial set of expansion points (assumed to be complex)
Compute initial projection matrices ,
, ,
Solve the quadratic eigenvalue problem:
Choose r eigenvalues and update expansion points
Repeat above steps while
Return reduced bases matrix and on convergence

## Slide 9: Results
Parameter – Beam length
Parameter range, P = [0.214 0.3 0.4 0.5 0.6 0.75 0.9 1.25]
Models evaluated at L = 1m and 100 elements
All models give approximately the same results
Accuracy of reduced-order models decreases at high frequencies

## Slide 10: Extrapolation Results
Models evaluated at L = 1.5m and 100 elements
Accuracy of all reduced-order models is worse than the interpolation case before
Accuracy of reduced-order models decreases even further at high frequencies (>4000 rad/s)
Accuracy of local pMOR is the worst since it is based on interpolation and thus, is unable to extrapolate the results

## Slide 11: Performance Study – Offline Computation Time
Time taken to assemble the parametric model and reduce it.
Higher for local pMOR since it requires further steps like transformation and interpolation as compared to global pMOR
After pMOR, obtained reduced model size:

## Slide 12: Performance Study – Online Computation Time
Time to solve and compute the frequency response of the reduced system.
Higher for global pMOR since the size of reduced system is more as compared to local pMOR
Number of elements doesn’t affect the size of reduced system and thus, it doesn’t affect online times as well
Variations in global pMOR online time are probably due to processor usage by other processes

## Slide 13: Performance Study – Total Computation Times
For small-sized systems, solving the full order system takes less time compared to pMOR techniques due to overhead involved in setting up the MOR
But as the number of elements increase, both local and global pMOR take considerable less time compared to the full order system
Local pMOR is taking more time than global pMOR since online computation is done only once in our case but with repeated online phase, global pMOR will take considerably longer than local pMOR
SO-IRKA takes least because it is performing MOR for just a single parameter

## Slide 14: Parametric Study
Parameter – Thickness of the beam

## Slide 15: Conclusions
Both pMOR techniques have been successfully implemented
Furthermore, we observe that pMOR techniques are quite effective and result in considerable resource-saving specially if the parameter range is chosen appropriately
Local pMOR is the best MOR technique for applications like optimization, navigation, etc. that require repeated model evaluations in online phase
Since online computation time is less compared to global pMOR and the offline phase can be carried out beforehand
This is true specially if extrapolation isn’t involved

## Slide 16: Thank You